## Slide 1
UrbanEV-v2: Agent-Based EV Charging Simulation for Maryland + DC
Enhanced MATSim Framework with PHEV Support, Dynamic En-Route Charging, and Equity Analysis
130,837 EV Agents | 9.8M Link Network | 1,958 Chargers | EPSG:26985
University of Maryland | 2025

## Slide 2
Original UrbanEV-v2 Framework
Developed by TU Munich / Chalmers / Gothenburg (Adenaw et al., 2020)
Core Architecture (MATSim 12.0 Extension)
- Agent-based co-evolutionary learning (plan selection + mutation)
- QSim traffic simulation with EV battery discharge model
- Charger infrastructure with plug-level queue management
- Variable-speed charging curves (Tesla, Leaf, generic profiles)
Original Scoring Function
- Range anxiety: penalty when SoC < threshold
- Empty battery: severe penalty at SoC = 0
- Walking distance: exponential decay to charger
- Home charging bonus: reward for using home charger
- Energy balance: penalty if end-of-day SoC < start
Original Strategies
- ChangeChargingBehaviour: add/remove/move charging at destinations
- SelectExpBeta: probabilistic plan selection
- Two subpopulations: nonCriticalSOC / criticalSOC

## Slide 3
Limitations of Original UrbanEV-v2
1. No En-Route Charging
Agents could only charge at destinations they already visited.
No mid-trip DCFC stops for long-distance trips.
2. No PHEV Support
All EVs treated as battery-only. PHEVs strand when battery depleted.
3. No Multi-Day SoC Persistence
Battery state reset each iteration. No overnight charging model.
4. No Charging Cost Differentiation
Flat pricing, no power-tier pricing, no time-of-use awareness.
5. Single-Thread Performance
parallelEventHandling forced to 1 thread. Dijkstra routing.
6. No Charger Reliability / Workplace Competition
All chargers 100% available. Private per-agent work chargers.

## Slide 4
Our Contributions: 12 Major Enhancements
New Simulation Features (Java)
1. InsertEnRouteCharging strategy (DCFC preference, dynamic duration)
2. PHEV gas fallback (CD/CS mode at 15% SoC)
3. Multi-day SoC persistence with overnight home charging
4. Workplace charger competition (shared pools, 1:5 ratio)
5. Charging cost awareness (softmax cost-weighted selection)
6. Charger reliability/downtime (80% DCFC, 92% L2 uptime)
Scoring Calibration (Literature-Backed)
7. betaMoney: sqrt income elasticity (Kickhofer et al. 2011)
8. emptyBatteryUtility: -15 to -40 (NREL BEAM)
9. homeChargingUtility: +1 to +2.5 (Ge et al. 2023)
10. Walking disutility recalibration (Geurs & van Wee 2004)
Performance & Infrastructure
11. FastAStarLandmarks + 14 parallel threads (100x speedup)
12. Queue traffic dynamics (fixes 95% stuck agent rate)

## Slide 5
Feature 1: Dynamic En-Route Charging
Problem: Agents with long trips run out of battery mid-drive.
Our Solution: InsertEnRouteChargingModule
Pipeline per agent:
1. SocProblemCollector records agents with SoC < threshold
2. Find the car leg where battery depleted
3. Scan route for chargers (DCFC preferred, L2 fallback)
4. Select charger based on risk attitude:
risk_averse: earliest 25% | moderate: middle 50% | risk_neutral: latest 25%
5. Dynamic duration from remaining distance + energy need + safety buffer
6. Split leg: [drive] -> [charge at DCFC] -> [drive]
Results: 5,054 insertions in iteration 1
85% DCFC, 15% L2 fallback
Duration: 5 min (quick top-up) to 22 min (long trip)

## Slide 6
Features 2-3: PHEV Gas Fallback + SoC Persistence
PHEV Gas Fallback (Axsen et al. 2020; Raghavan & Tal 2020)
- PHEVs switch to gasoline at 15% SoC (configurable)
- Gasoline consumption: energy / (34.2 MJ/L x 0.30 efficiency)
- 40K PHEV agents (30% of fleet) now behave realistically
Multi-Day SoC Persistence (Baum et al. 2022)
- End-of-iteration SoC carried to next iteration
- Overnight home charging model (NREL 2023; INL 2015):
SoC-dependent plug-in probability:
<30%: 95% | 30-50%: 85% | 50-70%: 65% | >90%: 10%
Produces 72% nightly plug-in rate (matches INL 70-75%)
Target SoC: Tesla 80%(60%)/90%(25%)/100%(15%)
Non-Tesla: 80%(40%)/90%(25%)/100%(35%) | PHEV: 100%
L1 max 11 kWh | L2 max 58 kWh overnight
No-home-charger agents (19%): no overnight recovery

## Slide 7
Features 4-6: Workplace, Cost Awareness, Reliability
Workplace Charger Competition (Wood et al. 2018, NREL)
- Shared pools: 1 plug per 5 EV workers (replaces per-agent private)
- 2,989 pools from 11,537 EV workers | First-come-first-served
Charging Cost Awareness (Ge et al. 2023; Chakraborty et al. 2020)
- Softmax cost-weighted selection: weight = exp(-beta x cost)
- Work (free) >> Home ($0.13) >> Public L2 ($0.25) >> DCFC ($0.48)
Charger Reliability (Rempel et al. 2022, NREL TP-5400-83459)
- Per-plug stochastic downtime each iteration
- DCFC: 80% uptime | L2: 92% uptime | Home: always available
- ~9% plugs disabled, ~280 chargers offline per iteration

## Slide 8
Scoring Parameter Calibration
Component Original Calibrated Source
-----------------------------------------------------------
Range Anxiety -5.0 -6.0 Dong & Lin 2020
Empty Battery -10.0 -40.0 NREL BEAM
Walking Dist. -1.0 -2.5 Charypar-Nagel
Home Charging +1.0 +2.5 Ge et al. 2023
Energy Balance -10.0 -4.0 Baum et al. 2022
Charging Cost flat power-tier MD rates
Detour Time -- -6.0/hr Axhausen et al.
Queue Wait -- VoT x 2.0 Lee & Small 2022
betaMoney Formula (Kickhofer et al. 2011, TRB)
Old: -6.0 x (62500 / income) range -50 to -1.5
New: -1.0 x sqrt(125000 / income) range -4.1 to -0.5
Reference: $125K (actual median of MD EV agents)

## Slide 9
Maryland + DC Data Pipeline
Input Data
- Synthetic population: 19.9M rows, 6.1M persons (BMC v3)
- OSM road network: 4.9M nodes, 9.8M links, 284 MB
- AFDC chargers: 1,958 (1,607 L2 + 283 DCFC + 68 Tesla)
Household-Level EV Assignment
- 362K has_ev=1 persons -> 142,754 actual EVs (ev_count)
- Top drivers per household get EV | Secondary: generic type
- Final: 130,837 agents (91K BEV + 40K PHEV)
Derived Attributes
- homeChargerPower: f(dwelling, ownership, income)
59% L2, 22% L1, 19% none
- betaMoney: -1.0 x sqrt(125000/income)
- rangeAnxietyThreshold: f(income, age) [0.10-0.40]
- riskAttitude: neutral/moderate/averse

## Slide 10
Performance Optimization
Bottleneck Before After Speedup
----------------------------------------------------------------------
Routing Dijkstra (1 thread) FastAStarLandmarks ~100x
(14 threads)
PrepareForSim 6.5 sec/person 0.17 sec/person ~38x
Event handling 1 thread (forced!) 14 threads ~14x
Traffic dynamics kinematicWaves queue fixes
(95% stuck) (0.04% stuck) stuck
Root Causes Found
- GotEVMain forced parallelEventHandling to 1 thread
- numberOfThreads=0 meant single-threaded, not auto-detect
- 65% of network links < 20m: kinematic wave storage gridlock
- SmartChargingScheduler ConcurrentModificationException
Hardware: Ryzen 7 2700X (16 threads), 128 GB RAM, JDK 17

## Slide 11
Agent Population & Equity Profile
Home Charger Distribution
L2 (7.2 kW): 76,787 (59%) | L1 (1.4 kW): 29,333 (22%) | None: 24,717 (19%)
Per-Component Scoring (Iteration 5)
Agent Group Score Empty Battery Home Bonus
--------------------------------------------------------
Has charger + uses -0.51 -0.83 +1.07
Has charger, unused -2.02 -1.05 0.00
NO home charger -10.46 -7.59 +0.17
Key Equity Findings
- No-charger agents score 20x worse than home-charger agents
- 69% of <$25K income agents have no home charger
- 85% of renters have no home charger
- 100% of apartment dwellers have no home charger
- 24,717 agents entirely dependent on public infrastructure

## Slide 12
Research Outputs & Future Studies
Charging Behavior (Iteration 5)
Public: 16,726 sessions | Home: 8,562 | Work: 8,142
En-route: 5,054 insertions (85% DCFC, 15% L2)
Overnight plug-in rate: 72% (matches NREL 70-75%)
Potential Studies
1. Charger infrastructure gap analysis
2. Income-stratified charging equity assessment
3. Grid load profiles (24-hr charging demand curves)
4. PHEV vs BEV electrification rates
5. Home charger penetration impact
6. Charger utilization & revenue modeling
7. Range anxiety geography (corridor SoC profiles)
8. Fleet composition impact on infrastructure
github.com/Tomal121186621/UrbanEV-MATSim-Maryland

## Slide 13
Thank You
github.com/Tomal121186621/UrbanEV-MATSim-Maryland
130,837 EV Agents | 33 Vehicle Types (BEV + PHEV)
9.8M Link Network | 1,958 Chargers | 14 Through Stations
8 Scoring Components | 3 Replanning Strategies | 6 New Features
Built on MATSim 12.0 + UrbanEV-v2 (TU Munich / Chalmers)