## Slide 1
UrbanEV-v2 Maryland: Simulation Results
Auto-generated after iteration 5 | 130,837 EV Agents | 30 Iterations
Iterations completed: 6
Total en-route insertions: 30,660
Home charging sessions: 40,036
No-charger-found errors: 53,982
Charger-full retries: 0
github.com/Tomal121186621/UrbanEV-MATSim-Maryland

## Slide 2
Score Convergence
Avg best should stabilize or improve as agents learn charging strategies
Iter Avg Executed Avg Worst Avg Average Avg Best
-----------------------------------------------------------------
0 -1.258 -1.258 -1.258 -1.258
1 -2.138 -2.828 -1.942 -1.056
2 -3.253 -4.795 -2.778 -0.874
3 -4.272 -6.628 -3.535 -0.661
4 -4.984 -8.187 -4.149 -0.408
5 -5.494 -9.539 -4.671 -0.180
Avg Best trend: -1.258 -> -0.180 (IMPROVING)

## Slide 3
Multi-Day SoC Persistence & Overnight Charging
End-of-day SoC carried to next iteration with realistic overnight recharging
Iter Vehicles Plugged In Plug Rate Home Charged No Charger
---------------------------------------------------------------------------
0 130,837 76,109 58.2% 76,109 24,717
1 130,837 53,632 41.0% 53,632 24,717
2 130,837 48,858 37.3% 48,858 24,717
3 130,837 45,798 35.0% 45,798 24,717
4 130,837 43,745 33.4% 43,745 24,717
5 130,837 42,522 32.5% 42,522 24,717
Overnight charging model (NREL 2023; INL 2015):
SoC-dependent plug-in probability: <30%=95%, 30-50%=85%, 50-70%=65%, >90%=10%
Target SoC: Tesla 80/90/100%, Non-Tesla 80/90/100%, PHEV 100%
L1 max 11 kWh overnight | L2 max 58 kWh overnight

## Slide 4
SoC Problems & En-Route Charging
Agents with depleted batteries get mid-trip DCFC stops inserted
Iter SoC Problems En-Route Insertions (cumulative)
-------------------------------------------------------
1 24,438
2 24,753
3 24,505
4 25,066
5 25,280
6 25,322
Total en-route insertions: 30,660
En-route charging features:
- DCFC preferred, L2 fallback only when no DCFC on route
- Dynamic duration from remaining distance x consumption rate
- Risk-based charger selection:
risk_averse (16%): earliest 25%, 30% buffer
moderate (48%): middle 50%, 15% buffer
risk_neutral (36%): latest 25%, 5% buffer

## Slide 5
Stuck Agents (Network Performance)
Queue traffic dynamics eliminated the 95% stuck rate from kinematic waves
Iter Stuck Agents % of 130,837
----------------------------------------
Traffic dynamics: queue (fixes kinematic wave short-link gridlock)
flowCapacityFactor: 1.0 | storageCapacityFactor: 1.0
stuckTime: 900s | removeStuckVehicles: true

## Slide 6
Charging Infrastructure Performance
Workplace competition, charger reliability, and infrastructure gaps
Workplace Charging
MobsimScopeEventHandling:224 Workplace charging: created 2989 shared charger pools (ratio 1:5) from 11537 EV workers
Charger Reliability (per iteration)
ChargerReliabilityManager:109 ChargerReliability: iteration 0 914/9789 plugs disabled (9.3%), 273 chargers fully offline
ChargerReliabilityManager:109 ChargerReliability: iteration 1 907/9789 plugs disabled (9.3%), 283 chargers fully offline
ChargerReliabilityManager:109 ChargerReliability: iteration 2 944/9789 plugs disabled (9.6%), 273 chargers fully offline
ChargerReliabilityManager:109 ChargerReliability: iteration 3 938/9789 plugs disabled (9.6%), 258 chargers fully offline
ChargerReliabilityManager:109 ChargerReliability: iteration 4 903/9789 plugs disabled (9.2%), 215 chargers fully offline
Charger Errors
No charger found: 53,982 total across all iterations
Charger full retries: 0
Public chargers: 1,607 L2 + 283 DCFC + 68 DCFC_TESLA = 1,958 total
Home chargers: 76,787 L2 + 29,333 L1 = 106,120 agents with home charging
Workplace pools: 2,989 shared charger pools (1:5 ratio)

## Slide 7
Summary — After Iteration 5
Auto-updated | github.com/Tomal121186621/UrbanEV-MATSim-Maryland
Simulation Progress: 6 of 30 iterations complete
Key Metrics (latest iteration):
Avg executed score: -5.494
Avg best score: -0.180
SoC problems: 25,322
En-route insertions: 30,660
Home sessions: 40,036
Features Active:
[x] PHEV gas fallback (40K PHEV agents)
[x] Multi-day SoC persistence + overnight charging
[x] Workplace charger competition (1:5 ratio)
[x] Cost-aware charging (softmax weighted)
[x] Charger reliability (80% DCFC, 92% L2)
[x] Dynamic en-route charging (DCFC preferred)
[x] Research-backed scoring calibration (8 params)